## Slide 1: Robot Car-3 AI & Robotics Centre of Excellence
GPREC & ZAS Robotics Collaboration
Training Schedule

## Slide 2: Navigational Robot Car-3
Review the Contents in the Box
Review & Discuss the Motor Controller Board, Assembly, Power Supply etc.
Discuss the Health & Safety Precautions
Practice the Following Lab
  Car Basic Movements; how to correct directions (by swapping the pins)
  Constant Speed via PID Controller
  Read & Display – GPS (Discuss the importance of removing GPS module while uploading)
  Read & Display – Digital Compass Bearing

## Slide 3: Navigational Robot Car-3
Arduino Nao
JGA25-370 6V 130 RPM Encoder Motors
TB6612 Motor Driver
OLED
NEO-6M GPS Module
MPU6050 – Accelerometer
QMC5883 – Digital Compass
Rotary Encoder
Battery Case
Batteries
Battery Charger

## Slide 4: Navigational Robot Car-3
Opportunities to Master
Encoder Motors Familiarity
Close Loop Control Systems (PID)
IMU Calibration
Sensor Fusion (Filters: Complementary/Kalman/EKF etc.)
Robot Motion Model
Odometry Calculations
Path Planning Algorithms

## Slide 5: Health & Safety

## Slide 6: Health & Safety
Batteries charging
GPS – disconnect whole uploading program to Nano
If the encoder motors behaviour is random, please check your battery status and may need charging
Beware of encoder motors 6 pin cable as there are 2 version:
Same Side
Opposite Side
If you have connected 6 pin cable, and the LED indicators are not ON, then you are likely using an incorrect 6-pin cable

## Slide 7: Motor Driver

## Slide 8: Navigational Robot Car-3
JGA25-370 6V 130 RPM Encoder Motors
Cable Type – JST PH 2.0 – 6 PIN (Same Side)
When Powered the LEDs on Encoder must light up

## Slide 9: Navigational Robot Car-3
TB6612 Motor Driver and DC370 Motor Connections with Arduino Nano
Left Motor
A-IN1 – Arduino Nano D8
A-IN2 – Arduino Nano D7
PWMA – Arduino Nano D6
L-Encoder-A - Arduino Nano D2
L-Encoder-B - Arduino Nano D4
Right Motor
B-IN1 – Arduino Nano D12
B-IN2 – Arduino Nano D10
PWMB – Arduino Nano D11
R-Encoder-A - Arduino Nano D3
R-Encoder-B - Arduino Nano D5

## Slide 10: Navigational Robot Car-3
Gear Ratios
Ger Ratio Tables

## Slide 11: Test Basic Movement

## Slide 12: Test Basic Movements
The purpose of this program is to test basic movements of the robot car
Also to ensure, your program is using the correct allocated PINs for Motor Inputs (IN1/IN2)
The Program has the following 3 major functional blocks
Pins declaration
  Ensure correct pins are defined (see sample program)
B. Setup:
input/outputs
C. Loop:
In the loop the car drives forward/left/right
Note: Please test each direction in isolation
Forward
Left
Right
If incorrect direction, then swap IN1/IN2 pins of the corresponding motor

## Slide 13: Basic Encoder Motors Functionality

## Slide 14: Basic Encoder Motors Functionality
The purpose of this program is to test basic encoder motor functionality
Also to ensure, your program is using the correct allocated PWM and Encoder PINs
The Program has the following 3 major functional blocks
Pins declaration
  Ensure correct pins are defined (see sample program)
OLED Initialisation for the feedback
B. Setup:
definition of interrupt routines to capture the encoder ticks
C. Loop:
In the loop, as you rotate the left/right motor, you will see the encoder tick counts going up/down depending on the direction of rotation

## Slide 15: Simple PID Controller

## Slide 16: Simple PID Controller for Straight Line Movement
The purpose of this program is to test basic encoder motor functionality
Also to ensure, your program is using the correct allocated PWM and Encoder PINs
The Program has the following 3 major functional blocks
Pins declaration
  Ensure correct pins are defined (see sample program)
OLED Initialisation for the feedback
B. Setup:
definition of interrupt routines to capture the encoder ticks
C. Loop:
In the loop, as you rotate the left/right motor, you will see the encoder tick counts going up/down depending on the direction of rotation

## Slide 17: Test GPS

## Slide 18: GPS Module
#include <TinyGPS++.h>
#include <Wire.h>
#include <Adafruit_GFX.h>
#include <Adafruit_SSD1306.h>
// ------------------- OLED SETTINGS -------------------
#define SCREEN_WIDTH 128
#define SCREEN_HEIGHT 64
#define OLED_RESET -1 // Reset pin (not used)
Adafruit_SSD1306 display(SCREEN_WIDTH, SCREEN_HEIGHT, &Wire, OLED_RESET);
// ------------------- GPS SETTINGS -------------------
TinyGPSPlus gps;
void setup() {
Serial.begin(9600); // GPS connected to Arduino RX (D0) and TX (D1)
delay(1000);
// Initialize OLED
if (!display.begin(SSD1306_SWITCHCAPVCC, 0x3C)) { // Common I2C address: 0x3C
Serial.println(F("SSD1306 allocation failed"));
for (;;); // Don't continue
}
display.clearDisplay();
display.setTextSize(1);
display.setTextColor(SSD1306_WHITE);
display.setCursor(0, 0);
display.println(F("GPS Module Test"));
display.display();
delay(1500);
}
void loop() {
// Read GPS data from Serial
while (Serial.available() > 0) {
gps.encode(Serial.read());
if (gps.location.isUpdated()) {
display.clearDisplay();
display.setTextSize(1);
display.setTextColor(SSD1306_WHITE);
display.setCursor(0, 0);
// Latitude
display.print(F("Lat: "));
if (gps.location.isValid())
display.println(gps.location.lat(), 6);
else
display.println(F("Invalid"));
// Longitude
display.print(F("Lon: "));
if (gps.location.isValid())
display.println(gps.location.lng(), 6);
else
display.println(F("Invalid"));
// Date
display.print(F("Date: "));
if (gps.date.isValid()) {
display.print(gps.date.day());
display.print("/");
display.print(gps.date.month());
display.print("/");
display.println(gps.date.year());
} else {
display.println(F("Invalid"));
}
// Time (UTC)
display.print(F("Time: "));
if (gps.time.isValid()) {
if (gps.time.hour() < 10) display.print("0");
display.print(gps.time.hour()); display.print(":");
if (gps.time.minute() < 10) display.print("0");
display.print(gps.time.minute()); display.print(":");
if (gps.time.second() < 10) display.print("0");
display.println(gps.time.second());
} else {
display.println(F("Invalid"));
}
display.display(); // Show all text on OLED
// Optional: Print to Serial as well
Serial.print("Lat: "); Serial.print(gps.location.lat(), 6);
Serial.print(", Lon: "); Serial.print(gps.location.lng(), 6);
Serial.print(", Date: ");
if (gps.date.isValid()) {
Serial.print(gps.date.day()); Serial.print("/");
Serial.print(gps.date.month()); Serial.print("/");
Serial.print(gps.date.year());
} else Serial.print("Invalid");
Serial.print(", Time: ");
if (gps.time.isValid()) {
Serial.print(gps.time.hour()); Serial.print(":");
Serial.print(gps.time.minute()); Serial.print(":");
Serial.print(gps.time.second());
} else Serial.print("Invalid");
Serial.println();
}
}
}
Get GPS Coordinates from GPS Module
Note: The GPS module MUST be disconnected from the controller board otherwise the program upload fails
Code Link: https://github.com/info-zas/zas-robotics-car-3-encoders-imu-gps/blob/main/04_BasicFunctionalTests/00_UnitTests/02_GPS_TX_RX_OLED.ino

## Slide 19: Digital Compass

## Slide 20: Digital Compass
#include <Wire.h>
#include <QMC5883LCompass.h>
#include <Adafruit_GFX.h>
#include <Adafruit_SSD1306.h>
// --- OLED ---
#define SCREEN_WIDTH 128
#define SCREEN_HEIGHT 64
#define OLED_RESET -1
Adafruit_SSD1306 display(SCREEN_WIDTH, SCREEN_HEIGHT, &Wire, OLED_RESET);
// --- Magnetometer ---
QMC5883LCompass compass;
// --- Calibration (runtime min/max) ---
int16_t xMin = 32767, xMax = -32768;
int16_t yMin = 32767, yMax = -32768;
int16_t zMin = 32767, zMax = -32768;
void setup() {
Serial.begin(9600);
Wire.begin();
if (!display.begin(SSD1306_SWITCHCAPVCC, 0x3C)) {
// If this fails, reduce what you print or switch to U8g2 low-memory mode
while (1);
}
display.clearDisplay();
display.setTextSize(1);
display.setTextColor(SSD1306_WHITE);
display.setCursor(0,0);
display.println(F("QMC5883L Calib"));
display.println(F("Rotate in all axes"));
display.display();
compass.init();
delay(800);
}
void loop() {
compass.read();
int x = compass.getX();
int y = compass.getY();
int z = compass.getZ();
// --- Update min/max ---
if (x < xMin) xMin = x; if (x > xMax) xMax = x;
if (y < yMin) yMin = y; if (y > yMax) yMax = y;
if (z < zMin) zMin = z; if (z > zMax) zMax = z;
// --- Offsets (hard-iron) ---
float xOff = (xMax + xMin) * 0.5f;
float yOff = (yMax + yMin) * 0.5f;
float zOff = (zMax + zMin) * 0.5f;
// --- Scales (soft-iron) ---
float xScale = (xMax - xMin) * 0.5f;
float yScale = (yMax - yMin) * 0.5f;
float zScale = (zMax - zMin) * 0.5f;
// Use averaged scale to keep math light on Uno
float avgScale = (xScale + yScale + zScale) / 3.0f;
if (avgScale < 1.0f) avgScale = 1.0f; // safety
// --- Calibrated & normalized readings ---
float xCal = (x - xOff) / avgScale;
float yCal = (y - yOff) / avgScale;
// zCal not needed for 2D heading on a level surface
// --- Bearing from calibrated X/Y ---
float bearing = atan2f(yCal, xCal) * 180.0f / PI;
if (bearing < 0) bearing += 360.0f;
// --- OLED output (compact) ---
display.clearDisplay();
display.setCursor(0,0);
display.print(F("Bear: ")); display.print(bearing, 1); display.println(F(" deg"));
// Show calibrated values briefly (helps verify offsets)
display.print(F("Xc:")); display.print(xCal, 2);
display.print(F(" Yc:")); display.println(yCal, 2);
display.print(F("Xmn:")); display.print(xMin);
display.print(F(" Xmx:")); display.println(xMax);
display.print(F("Ymn:")); display.print(yMin);
display.print(F(" Ymx:")); display.println(yMax);
display.print(F("Zmn:")); display.print(zMin);
display.print(F(" Zmx:")); display.println(zMax);
display.display();
delay(250);
}
A Sample Program to Get the post of the robot with respect to North (Bearing Angle)
Code Link: https://github.com/info-zas/zas-robotics-car-3-encoders-imu-gps/blob/main/04_BasicFunctionalTests/00_UnitTests/03_DigitalCompass_QMC_BearingAngle.ino